## Slide 1: How to Write Great Comments for Field Plan Reviews
Office of Engineering Services
2021

## Slide 2: WHAT YOU WILL LEARN
Why great comments are important
What makes a comment great
How to write great comments
How to take bad comments and make them great

## Slide 3: WHY GREAT COMMENTS ARE IMPORTANT
Easy to understand
Help generate great responses
Lead to responses that are easy to backcheck
Make the reports more professional

## Slide 4: WHAT MAKES A GREAT COMMENT
Clear and concise
Stands alone
Is written so someone who hasn’t seen the plans can understand the comment
Provides facts, states the problem, and gives the Designer direction
Gives reasons, examples, and/or cites references

## Slide 5: WRITING GREAT COMMENTS
Think about how the Designer will respond to the comment
  Did you provide enough details?
  Did you give reasons why something should be done?
  Did you refer to a policy, standard or guideline?
Think about how the person reviewing the response would know that was a valid response
  Without the details in the comment, it’s hard to backcheck the response

## Slide 6: WRITING GREAT COMMENTS
Be descriptive
  Use LT or RT, existing or proposed
    The proposed catch basin at STA 50+00 LT…
    The note in the upper left hand corner of Drawing 15-0007…
Present information clearly
  State facts first, then the problem, then give the Designer an action to complete
    The proposed catch basin is shown at STA 50+00 LT on Drawing 13-0003 and at STA 50+75 LT on Drawing 22-0003. State which is correct in your response and revise the plans accordingly.

## Slide 7: WRITING GREAT COMMENTS – DO
Be consistent
  Use same font throughout comments/report – Arial
  Margins should be justified on both sides throughout the comments/report
  Use the same abbreviations throughout the comments/report
    STA 23+00 vs. Sta. 23+00 vs. station 23+00
    ROW vs. R/W
    TS-1 vs. Typical Section #1 vs. TS #1 vs. TS-01
    Wall #3 vs. Wall No. 3
    RCUT vs. R-cut vs. R-Cut

## Slide 8: WRITING GREAT COMMENTS – DO
Use good grammar
  Make sure all tenses of the verbs agree
  Singular vs. Plural
Be professional
  We tend to write like we speak
    Where does A-1 outflow into?
    It is not clear where outflow from Str. A-1 goes. Please clarify.
  Use the proper names for items
  Use exact pay item names where possible

## Slide 9: WRITING GREAT COMMENTS – DO
Break up long sentences into two or more
  Run-on sentences are hard to follow
Use punctuation
  Use commas or semi colons within a sentence
    For example, see Drawing 06-0005.
  Use periods at the end of a sentence

## Slide 10: WRITING GREAT COMMENTS – DO
Use correct references
  Drawing is the Drawing No. in the Title Block
  Sheet No. is in the upper right-hand corner
Provide comments by Drawing No.
  This ensures comments are put in the correct section of the report
Combine similar comments into one
  It is not necessary to have several comments about the same thing
  This makes the report cleaner and easier for the designer to respond
  Comments will not always be included in the report in the exact format that they were submitted

## Slide 11: WRITING GREAT COMMENTS – DO
If a comment is repeated on several drawings, use one General Comment with some examples of the error or issue.
Only put General Comments in a General Comments section. If the comment applies to only one location, put it under the appropriate Drawing No. heading.

## Slide 12: WRITING GREAT COMMENTS – DON’T
Don’t start a sentence with “Need to”
  Just say it
    Add a pay item…; Include a detail…; Obtain additional ROW…
Don’t use Pronouns
  I, We, You, He, She, Our
Don’t include questions
  Exception! They are ok in two places in the report:
    Environmental section about bridge construction access/permitting
    Construction Plans section about the Post Construction Stormwater Report

## Slide 13: WRITING GREAT COMMENTS – DON’T
Don’t include vague or generic comments
  Provide reasons and/or examples
  Refer to manuals/policies/standards, etc.
Don’t delete parts of the report/Don’t leave things blank
  Use N/A or None
  If you delete parts or leave things blank, it is not clear if comments were intended, but omitted unintentionally
Don’t randomly capitalize words
  Example: Show cut and Fill lines at all required locations on the drawings.

## Slide 14: WRITING GREAT COMMENTS – DON’T
Don’t include an arrow prior to the comment if the designer doesn’t have to respond to the comment
Don’t ask for an item to be removed from the plans if it is a PPG requirement
Don’t abbreviate words
  Approx. vs. approximately
  Traffic Ops vs. Traffic Operations
  Min vs. minimum

## Slide 15: WRITING GREAT COMMENTS – DON’T
Don’t simply say “Delete Note 3.”
  When you backcheck the plans, how can you be sure the note was deleted? The remaining notes will be renumbered.
  Add a brief description of the note to the comment.
    Delete Note 3 (driveway pavement material description) because there are no driveways on the project.
    OR
    Note 3 discusses required driveway pavement materials. There are no driveways on this project, therefore, the note should be deleted.

## Slide 16: WRITING GREAT COMMENTS – DON’T
Don’t include separate comments for every pay item that should be adjusted due to other comments in the report.
  There is a general comment in the SOQ section of the report that addresses this.
    Please ensure correct pay items and quantities are entered into AASHTOWare Project Estimation after the plans have been revised according to the FPR Inspection comments.
  Combine the original comment with a statement about payment.
    Add asphalt patching to be placed before any leveling or topping is done. Ensure payment is addressed accordingly. (Typical Section)
    Determine if the existing gate at STA 27+30 RT will be removed and reset, or if a new gate will be installed. Ensure the proper pay item is included for the work. There are currently no pay items addressing the gate. (13 series)

## Slide 17: WRITING GREAT COMMENTS – DON’T
Don’t use words like “safety” or “concerns”
  If we say something is unsafe, and there is an accident on the project, we have provided documentation for the lawyers
    Recommend a minimum of 4’ raised median with opposing lanes of traffic in lieu of 2’ wide raised median. Coordinate with District Traffic Operations to ascertain their concerns.
      End comment after Traffic Operations.
    Typical Sections specify grass in areas between 0’ to 4’ wide. For areas where turf is less than two feet wide, the safe maintenance and survival of a viable section of turf can be an issue. Consider widening the strip to at least 3 feet, infilling with stamped concrete.
      Do not put this comment in the report at all. This is common practice on GDOT projects and should not be documented as unsafe.

## Slide 18: WRITING GREAT COMMENTS – DON’T
Don’t be a lazy reviewer 
  Example: Delete General Note 4 if there are no driveways on this project.
    The SME reviewer should look at the plans and see if there are driveways or not. Only use this comment if there are no driveways. If using the comment, reword it to say “because” instead of “if”.
  Example: Ensure that the driveways over 11% are concrete.
    This is something that the SME reviewer can easily check. Only use this comment if there are driveways over 11% not shown as concrete.

## Slide 19: WRITING GREAT COMMENTS – DON’T
Don’t include comments that are not directed to the Designer
  District Utilities should do a complete review of Utility Plans. There have been issues when utilities are in the contract, and things are left out, such as pay items, notes, and details.
  Ensure District Traffic Ops has reviewed the plans to check for misspelled street names.
  Request GDOT include the revision dates on common cut and paste cells used in plan development.

## Slide 20: WRITING GREAT COMMENTS – DON’T
Don’t include comments that will leave discussions undocumented or offline
  Discuss issue at FPR and include in the report
  No one will know the outcome of the discussion if it is not in the report, and it will not be possible to check the plans to see if changes were made correctly
    Get with District Construction after the meeting to discuss staging options.
    Traffic Ops would like to discuss logistics of trucks entering the intersection.

## Slide 21: WRITING GREAT COMMENTS – DON’T
Don’t include comments that repeat the specifications
  No section of the spec book is more important than another, and the contractor must adhere to all of it. Calling it out on the plans implies importance and changes the hierarchy specified in the spec book.
    Contractor shall adhere to specification section 201- clearing and grubbing right-of way, 201.3 5A for eradication of invasive species if encountered.
    Per GDOT Specification Sections 700 and 702, lime and fertilizer are prohibited in multitrophic native planting areas, stream buffers, wetlands, wet swales or marshes. Wheat straw mulch is the only type of mulch allowed in native multitrophic or stream buffer restoration planting areas, per GDOT Specification section 702.3.05.C.

## Slide 22: WRITING GREAT COMMENTS – DON’T
Don’t include comments that you haven’t verified or you know are incorrect.
  Provide the fabric detail.
    The fabric detail is shown in Drawing 05-0004.
  Provide the guardrail detail for the new guardrail to be installed both on the shoulders and median.
    New guardrail is not proposed in this contract.
In both examples, the comments could have been easily verified by looking at the plans.

## Slide 23: BLUE BEAM COMMENTS TO AVOID
Please shift this OBF (NE of existing culvert) to reflect orange line shown that protects more buffer & ties to the existing roadway.
Add TP 10 RPMs surrounding the post.
D1-11 sign - Replace with W1-2/W16-8P sign assembly.
Add dividing line between each destination.
Only the initial letter of each word should be capitalized.

## Slide 24: BLUE BEAM COMMENTS TO AVOID
X – does this mean something should be deleted?
? – does this mean you are unsure about something?
T – does this represent a sign symbol?
Remember to be clear and concise
Remember to be descriptive with your comments
Designers get marked up plans, but others reading the report do not

## Slide 25: WRITING GREAT COMMENTS – THINGS TO THINK ABOUT
Comments that start with “recommend” or “consider”
  Recommendations are left up to the Designer to decide if they want to do them.
  Why would the Designer do them? Time is money. The Designer already thinks the plans are fine as is.
  If you feel strongly that something should be done or it is a requirement, just say to do it, leave off the “recommend”, but do provide compelling reasons why it should be done.
  If it really is just a recommendation or something to be considered, make sure you provide reasons why you are recommending it.

## Slide 26: WRITING GREAT COMMENTS – THINGS TO THINK ABOUT
Is the comment appropriate for this FPR?
  Preliminary - PFPRs are about setting ROW footprints
    There may be some plan presentation comments, but the comments should focus on footprint and determining if there is enough ROW to build the project
    Review constructability to ensure there is adequate ROW and that detours are accounted for
    Don’t make comments requesting items that are not required for the PFPR
      Lump Sum Bridge is allowed at PFPR
  Interim - IFPRs are “snapshots” of progress from the earlier FPRs
    Review should focus on what hasn’t been done from previous PFPR/SPFPR and policy changes
    This is an accountability review

## Slide 27: WRITING GREAT COMMENTS – THINGS TO THINK ABOUT
Is the comment appropriate for this FPR?
  Final - FFPRs are about finalizing plans and documents
    Special provisions should address all issues, time constraints, liquidated damages
    All required items should be shown and quantified in the SOQ and AASHTOWare
    ROW plans are approved and negotiations with property owners have started; changes should only be made where items are shown off the ROW/easement
      Not the time to redesign drainage if it will require additional ROW
    Should not include comments from previous FPRs with accepted responses unless those items have not been corrected
  Supplemental - SPFPR/SFFPR
    An additional review because of plan quality issues or time; follows the same rules as the PFPR or FFPR

## Slide 28: WRITING GREAT COMMENTS – THINGS TO THINK ABOUT
Vague words like “consider” or “verify”
  If the response is “will consider”, what have we gained by putting the comment in the report? Will the Designer just think about it? Do they have to make any changes?
  If the response is “will verify”, how do we know it was verified? If you look at the corrected plans after the FPR, and they are the same, how do you know if they verified it and it was ok, or if they forgot to verify it?

## Slide 29: WRITING GREAT COMMENTS – THINGS TO THINK ABOUT
Some words can be used as both nouns (objects) or verbs (actions)
    This can be confusing
Think about your choice of word
    - Note - Drain - Outfall
    - Detail - Work - Label
    - Access - Conflict - Pipe
    - Slope - Stripe - Document

## Slide 30: BAD COMMENT = BAD RESPONSE
Please add driveway typical section.
  Driveway typical sections will not be shown as they are not required per the PPG.
  When comments ask for things above and beyond the requirements, the comments should give reasons for these requests. This seems like something that wouldn’t take the Designer too much time to do, and would probably save the Construction folks some time out in the field. But without reasons why it should be done, there is nothing to compel the Designer to do the extra work.

## Slide 31: BAD COMMENT MADE BETTER
In order to ensure the proposed driveway at STA 17+21 LT is constructed properly, please add a typical section. This driveway is a commercial driveway, but appears to have been designed as a residential driveway.

## Slide 32: BAD COMMENT = BAD RESPONSE
At STA 592+00 LT, correct drainage issue.
  There is no drainage issue at 592+00 LT. No change needed.
  This ends up being an acceptable response because the comment wasn’t very clear. It should have described the issue. State the facts (what is wrong with the drainage) and then ask for it to be corrected. How can someone backcheck this with no details?

## Slide 33: BAD COMMENT MADE BETTER
There appears to be a low point at STA 592+00 LT, but there is no drainage structure shown. Review drainage in this area and determine if a structure should be added.

## Slide 34: BAD COMMENT = BAD RESPONSE
Ensure all drainage is accounted for on parcels. If there is an existing low point, or one is being developed due to the work, add the necessary drainage.
  Drainage will be accounted for. Any existing or newly created low points will be addressed to ensure proper drainage.
  This is just a wasted comment and response. How else would you respond to it? If the reviewer noted places where low points were being developed, or knew of existing low points, specific locations should be added to the comment. That would be more helpful than just a generic comment.

## Slide 35: BAD COMMENT MADE BETTER
Ensure all drainage is accounted for on all parcels. For example, it appears there is an existing low point at STA 81+17 LT, and one has been created due to the proposed construction at STA 111+63 RT. It may be necessary to add structures to ensure water doesn’t flow back into the roadway.

## Slide 36: BAD COMMENT = BAD RESPONSE
Coordinate with the Area Office to show rip rap in all applicable ditches during design not during construction.
  It is not in the scope of work to coordinate rip rap during design of this project. Rip rap will be designed per the GDOT drainage manual to protect proposed drainage structures and ditches.
  This would have been a better comment if the Area Office had provided locations where the rip rap would be needed. Then the response would be required to address each location.

## Slide 37: BAD COMMENT MADE BETTER
There are several ditches where rip rap will be needed to reduce erosion. See STA 57+01 LT, STA 68+23 RT and STA 99+01 RT. On similar projects, there have been issues with erosion in the ditches, and this should be addressed as part of the design for this project.

## Slide 38: BAD COMMENT = BAD RESPONSE
Ensure that District Traffic Operations has verified the correct sheeting for the signs versus sign codes.
Ensure that District Traffic Operations has verified all necessary Pay Items for striping.
  This comment should be stricken from the report. Did District Traffic Operations not receive FFPR plans to review and provide comments?
  These types of comments show up in almost every report. This is not something that is the responsibility of the Designer. District Traffic Ops gets the plans for FPRs; they should be reviewing the plans. Avoid putting comments like this in the report. If there are specific places where errors have been found, then those types of comments should be used.

## Slide 39: BAD COMMENT MADE BETTER
If you are facilitating the FPR, the best way to handle these types of comments is to discuss this at the FPR. If Traffic Ops has reviewed the signing and marking plans and has provided their comments, then use the comments.
If you are writing comments like this, and you have concerns, ask someone from Traffic Ops if they have reviewed the plans. And you can review every section of the plans, too, and provide comments.
There really is no good way to put these types of comments in the report.

## Slide 40: TAKE A BAD COMMENT & MAKE IT GREAT
Ensure to use latest General Note - Standard Signs. Note 3 has added information and Notes 4C and 14 have been revised.

## Slide 41: TAKE A BAD COMMENT & MAKE IT GREAT
Ensure to use latest General Note - Standard Signs. Note 3 has added information and Notes 4C and 14 have been revised.
  This is bad grammar; we don’t “ensure to use”

## Slide 42: TAKE A BAD COMMENT & MAKE IT GREAT
  Use latest General Note - Standard Signs. Note 3 has added information and Notes 4C and 14 have been revised.

## Slide 43: TAKE A BAD COMMENT & MAKE IT GREAT
Enlarge the SW quadrant radius and pull back the EB lanes in order to accommodate a channelizing island to shorten the proposed 140’ pedestrian crosswalk. Such a long crosswalk is undesirable in terms of pedestrian safety, and in terms of operations as it would result in very long side street phasing.

## Slide 44: TAKE A BAD COMMENT & MAKE IT GREAT
Enlarge the SW quadrant radius and pull back the EB lanes in order to accommodate a channelizing island to shorten the proposed 140’ pedestrian crosswalk. Such a long crosswalk is undesirable in terms of pedestrian safety, and in terms of operations as it would result in very long side street phasing.
  Don’t say the crosswalk is unsafe or undesirable. If we don’t change the plans, we have given a lawyer proof that we knew this crosswalk was unsafe.
  Delete references to safety

## Slide 45: TAKE A BAD COMMENT & MAKE IT GREAT
  Enlarge the SW quadrant radius and pull back the EB lanes in order to accommodate a channelizing island to shorten the proposed 140’ pedestrian crosswalk. The shorter crosswalk is more desirable, and would result in shorter side street phasing.

## Slide 46: TAKE A BAD COMMENT & MAKE IT GREAT
District Construction recommends 7 digit Pay Items be added to all Pay Items.

## Slide 47: TAKE A BAD COMMENT & MAKE IT GREAT
District Construction recommends 7 digit Pay Items be added to all Pay Items.
  No reasons given. When asking for something above and beyond what is required, you need to sell it. And “recommends” is left up to the designer. Would you do the extra work?

## Slide 48: TAKE A BAD COMMENT & MAKE IT GREAT
  District Construction requests that 7 digit Pay Items be added to all items in the SOQ to make it easier to determine if all required items have been accounted for in AASHTOWare.

## Slide 49: TAKE A BAD COMMENT & MAKE IT GREAT
Ensure that all traffic signal equipment is shown within the right-of-way.

## Slide 50: TAKE A BAD COMMENT & MAKE IT GREAT
Ensure that all traffic signal equipment is shown within the right-of-way.
  Is there something that’s not? If so, state where. If not, why put this comment in the report? We don’t have a comment saying all walls, pipe, signs, etc., should be within the ROW.

## Slide 51: TAKE A BAD COMMENT & MAKE IT GREAT
Ensure that all traffic signal equipment is shown within the right-of-way. For example, the cabinet located at STA 115+75 LT is off the right-of-way.

## Slide 52: TAKE A BAD COMMENT & MAKE IT GREAT
Further discussion needs to be had on the possibility of improving the staging plans.

## Slide 53: TAKE A BAD COMMENT & MAKE IT GREAT
Further discussion needs to be had on the possibility of improving the staging plans.
  How would you respond to this?
  How would someone reading the report know what was wrong?
  What are the issues to be improved?
  How do you backcheck this?
When a comment makes you ask a lot of questions, you know the Designer is going to be asking questions, too!

## Slide 54: TAKE A BAD COMMENT & MAKE IT GREAT
  The staging plans should be improved by:
    Moving all side road detours to Stage 2
    Using temporary pavement for the shift at Sta 270+00
    Adding a final stage for surface course and striping
  This would minimize disruption during Stage 1, and allow for better traffic flow.

## Slide 55: TAKE A BAD COMMENT & MAKE IT GREAT
Verify how quantity was obtained for flowable fill.
  State if it appears to be too high or too low. Just add another sentence.
  Verify how quantity was obtained for flowable fill. It appears to be too high.
Increase Foundation Backfill quantity to 100 CY.
  Why? Give a reason. Is more specified in the soil survey? Is this request based on past experience with other projects in this area?
  In accordance with the soil survey, increase Foundation Backfill quantity to 100 CY.

## Slide 56: TAKE A BAD COMMENT & MAKE IT GREAT
The southeast quadrant needs to stripe out radius.
  It is not possible for a quadrant to perform striping!
  In the southeast quadrant, the radius should be striped out.
  OR
  The radius in the southeast quadrant should be striped out.

## Slide 57: EXAMPLES OF GREAT COMMENTS
TS 1 shows full depth pavement beginning at STA 461+00; however, full depth pavement is shown on 13-0001 beginning at STA 460+00. Respond with the correct station and revise the plans to match.
Coordinate with District Traffic Operations to determine which existing turn lanes should be maintained during construction. For example, Stage 1 shows 10’ center turn lane; however, subsequent stages do not. In the response, provide a list of those to be maintained.

## Slide 58: EXAMPLES OF GREAT COMMENTS
Verify where the last warranting fill is proposed in the vicinity of STA 117+75 RT. (Refer to the bottom RT of GA Standard 4000W for warranting fill height criteria.) Based off of the determined location, further verify that the required runout length of w-beam rail (in accordance with the top right of GA Standard 4000W) has been provided in advance of the warranting area. It appears that the length of w-beam provided is just shy of meeting the required runout length.

## Slide 59: EXAMPLES OF GREAT COMMENTS
The tops of catch basins in radius returns have a tendency to collapse when impacted by truck turning movements. Use a GaStd 1019B TP V-1 Drop inlet in proposed radius returns. For example, see Drawing 13-0001 Str A-0.2A.
Do not use GaStd 9031U Junction boxes as they do not provide access to pipes. Recommend using GaStd 1019B TP V-1 Drop inlets or GaStd 1011A Manholes. See Drawing 22-0007 comment regarding Str R-8 for additional information.

## Slide 60: EXAMPLES OF GREAT COMMENTS
Per GDOT PPG, revise the paving quantities table to include paving quantities per each alignment. Currently, the table gives quantities per construction plan drawing. Instead, the mainline and each side road should be listed with totals given per alignment.

## Slide 61: EXAMPLES OF GREAT COMMENTS
Revise Type 12A terminals to ensure compliance with GA Standard 4384. Type 12A terminals must be 53 ft 1 ½ inches in length.
Revise driveway profiles per Section 17-0003 of the GDOT PPG so that each profile starts with STA 0+00 at the centerline of the roadway which the drive intersects. This means the mainline PGL and travel lane cross slope, etc., will be also be illustrated.

## Slide 62: A GREAT WAY TO GET A GREAT RESPONSE: ASK FOR IT!
Add “explain”, “indicate” or “document” to the comment
  Please document the final decision in the response.
  In the response, explain what this is to be used for.
  In the response, indicate if….
  Indicate which is correct in the response.

## Slide 63: EXAMPLES OF COMMENTS ASKING FOR EXPLANATIONS
Rockwell Road has been recently resurfaced. If the project database does not reflect this work, make the necessary corrections. In the response, state what additional work and corrections are required.
  We will confirm this in the field, and if needed, update the survey database and reflect the same in the corrected FFPR plans.
Explain the need for installing the earth check dam at STA 109+80 LT.
  The permanent earth check dam at Sta. 109+80 LT is being utilized as a ditch plug to direct water into B-IN structure to maintain existing condition water flow.
Provide a response that documents the results of the Phase II subsurface investigation at Parcel 5 and Parcel 7.
  Phase II investigation revealed no contamination at Site No. 5. At site No. 7, minimal soil contamination (not exceeding EPD regulatory limits) was noted at a depth of 25-feet. As such, ROW acquisition may proceed at these two sites. If USTs are encountered during construction, then it will be handled as per GDOT Standard Specifications, Section 217 – Removal of USTs. These notes will be added to the plans.

## Slide 64: TEST QUESTION - FIND THE ERRORS
The two lane circulating roadway configuration opposite the Walmart entry does not coincide with the upstream single lane approach feeding it from Walmart. This will cause crashes if it is built this way because it creates a weaving lane change at the downstream exit to Roswell Road. The Concept Report shows the correct lane configuration for safety and capacity. See Drawing 10-0005 for comments on the Walmart entry capacity deficiency at opening day. A single lane entry will congest immediately. Recommend to revise the Walmart entry to two lanes.

## Slide 65: TEST ANSWER
The two lane circulating roadway configuration opposite the Walmart entry does not coincide with the upstream single lane approach feeding it from Walmart. This will cause crashes if it is built this way because it creates a weaving lane change at the downstream exit to Roswell Road. The Concept Report shows the correct lane configuration for safety and capacity. See Drawing 10-0005 for comments on the Walmart entry capacity deficiency at opening day. A single lane entry will congest immediately. Recommend to revise the Walmart entry to two lanes.

## Slide 66: TEST ANSWER
The two lane circulating roadway configuration opposite the Walmart entry does not coincide with the upstream single lane approach feeding it from Walmart. This will cause crashes if it is built this way because it creates a weaving lane change at the downstream exit to Roswell Road. The Concept Report shows the correct lane configuration for safety and capacity. See Drawing 10-0005 for comments on the Walmart entry capacity deficiency at opening day. A single lane entry will congest immediately. Recommend to revise the Walmart entry to two lanes.

## Slide 67: TEST ANSWER
The two lane circulating roadway configuration opposite the Walmart entry does not coincide with the upstream single lane approach feeding it from Walmart. This will cause crashes if it is built this way because it creates a weaving lane change at the downstream exit to Roswell Road. The Concept Report shows the correct lane configuration for safety and capacity. See Drawing 10-0005 for comments on the Walmart entry capacity deficiency at opening day. A single lane entry will congest immediately. Recommend to revise the Walmart entry to two lanes.

## Slide 68: TEST COMMENT MADE GREAT
The two lane circulating roadway configuration opposite the Walmart entry does not coincide with the upstream single lane approach feeding it from Walmart. This creates a weaving lane change at the downstream exit to Roswell Road. The Concept Report shows the correct lane configuration. Revise the Walmart entry to two lanes, as shown in the concept report.

## Slide 69: CONCLUSION – KEY POINTS
Determine if the comment is right for the FPR
Clearly state facts and problems
Give examples and reasons, cite references
Verify the comment is acceptable as part of the permanent documented project records
Verify the comments you get from SMEs
Think about how you would respond
Think about how someone would backcheck the response

## Slide 70: QUESTIONS???