## Slide 1: NEPA 101: Environmental Overview for Federally Funded Projects
09.16.2025
Office of Program Delivery
(Part 1)
Notes: The purpose of this presentation is to provide an overview of the environmental process for federally funded projects. Part 1 of the training focuses on understanding what NEPA is and when it will be required. It also provides an understanding of the special studies process.
Training Time: 1.5 hour

## Slide 2: Learning Objectives
NEPA required
3 Levels of NEPA document
Process for Special Studies
A
E
A
N
H
Notes: (click 1) You will learn how to determine if NEPA is required.
(click 2) You will be able to list the 3 levels of NEPA documentation.
(click 3) You will be able to list the 5 special studies disciplines, and the environmental process associated with each of the special studies.

## Slide 3
NEPA required
Notes: First, let’s discuss when NEPA is required for a project.

## Slide 4: National Environmental Policy Act (NEPA)
federal law = environmental protection
NEPA's basic policy is to assure:
  proper consideration
  prior to undertaking any major federal action
Key Words: Significantly Affects the Environment
Notes: (click 1) The National Environmental Policy Act, aka NEPA, is a federal law that protects our environment.
(click 2) NEPA’s basic policy is to assure that the proper consideration is given to the environment prior to undertaking any major federal action that significantly affects the environment.
(click 3) The key words in the law is to consider and avoid significantly affecting the environment.

## Slide 5: When is NEPA needed?
Compliance with NEPA is mandatory when one of the following conditions is met:
Federal funds or assistance
Federal permit
Federal approval of an action
Federal funds or assistance eligibility maintained
Interstate encroachment
Notes: When is NEPA needed? Compliance with NEPA is mandatory when one of the following conditions is met:
(click 1) federal funds or assistance are used to fund a phase of the project. It does not matter which phase. The important trigger is the use of federal funds.
(click 2) if a federal permit is required, then NEPA is triggered regardless of how the project is funded.
(click 3) if a federal approval of an action is required; or
(click 4) federal funding or assistance eligibility must be maintained. In other words, if there is a chance that federal funds will be requested, follow the NEPA process avoid delays to the project.
(click 5) Whenever federal funds are used or when an interstate encroachment occurs, GDOT and FHWA are responsible for the preparation of NEPA documents.

## Slide 6: Why is NEPA needed?
There are two reasons for documenting the NEPA process:
Disclose the ENV analysis process
Present the results (i.e. decisions)
Notes: Why is NEPA needed?
(click 1) There are two reasons for documenting the NEPA process:
(click 2) to provide complete disclosure of the environmental analysis process, and
(click 3) to present the results or decision.

## Slide 7
3 Levels of NEPA document
Notes: Now that you understand what triggers a NEPA document, let’s discuss the types of the NEPA document.

## Slide 8: What are the Levels of NEPA Documentation?
CE
EA
EIS
Categorical Exclusion
Environmental Assessment
Environmental Impact Statement
Notes: There are 3 levels of NEPA documentation:
(click 1 – 3) CE, EA, and EIS. We will go into a little more detail about each on the following slides.

## Slide 9: Categorical Exclusion (CE)
A CE documents actions which do not involve significant environmental impacts, either individually or cumulatively.
Notes: A categorical exclusion documents actions which do not involve significant environmental impacts, either individually or cumulatively.

## Slide 10
PCE vs CE
CE
OES review
FHWA review
NEPA approval
PCE
OES review
NEPA approval
GDOT
FHWA
Notes: (click 1) The CE is the lowest level of the NEPA documentation. It is used for projects with minor impacts. It must be approved by FHWA.
(click 2) A programmatic categorical exclusion is a CE that does not require an FHWA signature for approval. OES approves PCEs. The PCE is typically prepared for projects that are very small in scale and have minor to no environmental impacts and little to no ROW.

## Slide 11: Environmental Assessment(EA)
Projects in which the significance of the environmental impact is not clearly defined.
The preparation of an EA is to determine the appropriate environmental document required.
Notes: The next level up from a CE is an Environmental Assessment or EA.
(click 1) Project in which the significance of the environmental impact is not clearly defined. The preparation of the EA is needed to determine the appropriate document required.
(click 2 & 3) The Environmental Impact Statement or EIS is required for projects who action will have significant effect on the environment.

## Slide 12
Environmental Impact Statement (EIS)
Projects whose action will have a significant effect on the environment.
Notes: The next level up from a CE is an Environmental Assessment or EA.
(click 1) Project in which the significance of the environmental impact is not clearly defined. The preparation of the EA is needed to determine the appropriate document required.
(click 2 & 3) The Environmental Impact Statement or EIS is required for projects who action will have significant effect on the environment.

## Slide 13: NEPA Review
Why is NEPA required on a project?
A. It is a federal law.
B. Required on projects involving federal funds or actions.
C. It is a GDOT policy.
D. A & B
E. B & C
Notes: (direction: Read question 1 and give participants time to respond.)
(click 1) Answer: D

## Slide 14
How many the levels of NEPA documentation are there?
1
2
3
4
EIS
EA
CE
Increasing level of impacts
NEPA Review
Notes: (direction: Read question 1 and give participants time to respond. )
(click 1) Answer: C - There are 3 levels. PCE is a subcategory of a CE. It is not a separate level of document.

## Slide 15
Who approves the NEPA document?
OES
Engineering Services
USACE
FHWA
NEPA Review
Notes: (direction: Read question 1 and give participants time to respond.)
(click 1) Answer: D - The Federal Highway Administration approves all NEPA documents. The exception is a PCE, which OES will approve.

## Slide 16
Process for Special Studies
A
E
A
N
H
Notes: Before a NEPA document is written, special studies must be completed. We will discuss the various disciplines that are known as the environmental special studies and the environmental process for each one.

## Slide 17: Environmental studies must be completed to determine the appropriate level of NEPA documentation.
Environmental Studies
NEPA Document Level
Leads to
Notes: (click 1) Until the environmental studies (resource ID and technical studies) are complete, the appropriate level of NEPA documentation cannot be confirmed. However, the NEPA analysist will know the anticipated level of NEPA document prior to the environmental studies being approved.

## Slide 18: NEPA Environmental Process: Overview
Resource ID Reports
Technical Studies Reports
NEPA Document
What resources exist on the project?
What are the impacts to resources?
How will the project affect various parts of the environment?
Special Studies
Notes: (click 1) The NEPA environmental process can be broken down into 3 main parts. First is resource ID. This answers the question of “what resources exist on the project?”
(click 2) Resource ID is followed by the technical studies report. These reports answer the question “what are the impacts to the resources?”
(click 3) The environmental special studies is comprised of both resource ID reports and technical studies reports. Both have to be completed to finish the special studies.
(click 4) NEPA document preparation and approval occurs after the special studies (specifically the technical studies) are approved. This slide shows the chronological order of the environmental process.

## Slide 19: Special Studies
Completed during the early stages
May occur in two phases: resource identification and evaluation of project impacts.
Provide key information
NEPA document summarizes these findings
Notes: (click 1) The studies need to be completed during the early stages of project development, beginning during concept development and continuing into preliminary design.
(click 2) Some studies occur in two phases: resource identification and evaluation of project impacts.
(click 3) These studies provide key information for use in project development as well as agency coordination.
(click 4) Within the actual NEPA document, the environmental findings are summarized in text.

## Slide 20: What is evaluated under Ecology?
Ecology resources include:
Waters of the US
State mandated buffers on streams and open waters
Protected species
Bats and their habitat
Migratory bird habitat
Permits and required mitigation
Notes: Ecology is a discipline that covers may different aspects of the biological environment. The ecologist will identify ecology resources related to:
Waters of the US which includes streams, wetlands, ponds, lakes, marshes and a few other things.
State mandated buffers are vegetated protective zones around streams and open waters (i.e. lakes and ponds)
Protected species such as aquatic species, birds, mammals, plants, etc.
Bats and their habitat
Migratory bird habitat
Permits and required mitigation for impacts to permitted ecology resources.

## Slide 21: What is Cultural Resources?
Physical and intangible evidence of past human activity that have scientific, historical, or traditional significance.
Cultural Resources are comprised of:
  Historical Resources
  Archaeological Resources
Notes: (click 1) Cultural Resources is the physical and intangible evidence of past human activity that have scientific, historical, or traditional significance. This evidence of how humans have related to their environment through their culture.
(click 2) Cultural Resources is broken into 2 different disciplines of historical resources which is studied by a historian and archaeological resources which is studied by an archaeologist.
(next slides will discuss history and archaeology in a little more depth)

## Slide 22: What is evaluated under History?
Historic resources included or eligible for inclusion in the State’s Historic Resource Survey or the National Register of Historic Places.
Examples include, but are not limited to:
  Buildings,
  Structures,
  Historic sites,
  Landscapes, &
  Districts
Notes: (click 1) Historic resources included or eligible for inclusion in the State’s Historic Resource Survey or the National Register of Historic Places. There are criteria that a historic resource must meet to be considered an eligible resource. Age of a structure is only one criteria that may need to be met.
(click 2) Examples of historic resources include but are not limited to:
  Buildings,
  Structures,
  Historic sites,
  Landscapes, &
  Districts

## Slide 23: What is evaluated under Archaeology?
Archaeological resources are the material evidence of human culture and activity in the past.
Examples include, but are not limited to:
  Cemeteries (these are also historic)
  Rock piles,
  Earth mounds,
  Broken pottery, &
  Remnants of house sites.
Notes: (click 1) Archaeological resources are the material evidence of human culture and activity in the past. Archaeological resources are found buried, on the surface of the land, or partially to totally submerged in water.
(click 2) Archaeological resource examples include, but are not limited to:
  Cemeteries (these are also historic resources)
  Rock piles,
  Earth mounds,
  Broken pottery, &
  Remnants of house sites.

## Slide 24: Order of Environmental Documentation
Special Studies Documents
NEPA Document
FHWA approval (environmental clearance)
Agency/FHWA approval
Field Studies
Notes: (click 1)This is a very simplified look at the environmental process. First the archaeologist, historian, and ecologist visit the site to conduct the field studies. In other words, each discipline is looking for potential resources within the project area.
(click 2) The resources and impacts are then documented in the special studies documents, as well as air and noise impacts. In this graphic, the resource ID and technical studies are both part of the special studies documents.
(click 3) The special studies reports must be reviewed and approved by the assigned agency.
(click 4) After the technical studies are approved, the NEPA document is written.
(click 5) The NEPA document is then submitted to FHWA for approval. Once it is approved, the project has received environmental clearance to proceed to the next phase.

## Slide 25: PDP Environmental Process
History Survey
Archaeology Survey
Concept Report
Resource ID Reports
ENV Field Surveys
*Generally, field surveys are done during concept development.
(ENV Information Shared)
Resource ID Process
Concept Phase
Layout/ ESB
Ecology Survey
Notes: (click 1) The first step of the environmental process is to identify any known or eligible resources within the study area of the project. The historian, ecologist, and archaeologist must physically visit the field to determine if there are any resources. This step is usually, but not always, done during the concept development phase.
(click 2) The information about the resources is documented in both the resource ID reports and summarized in the concept report.

## Slide 26: PDP Environmental Process (continued)
SHPO
FHWA/ USFWS/ GAEPD
Concept Report
Resource ID Reports
Assessment of Effect Reports & Air and Noise Studies
Resource ID:
Agency Review/Approval
Preliminary Design
Technical
Studies
History & Archaeology
Ecology
Tech Studies Process
Resource ID Process
A3M
Concept Phase
Notes: (click 1) After the resource ID reports are written, each report must be submitted to the appropriate agency for review and approval. The agencies have final approval on whether a resource is considered a resource or not. This is occurring while the preliminary design has started.
(click 2) Once the agencies approve all 3 of the resource ID reports, the A3M meeting is held with the designer and the environmental team. This is an opportunity to discuss ways to minimize or avoid impacts through the design.
(click 3) After the plans are updated based on the A3M meeting, the technical studies are written to document the proposed impacts to the resources.

## Slide 27: PDP Environmental Process (continued)
GDOT
SHPO
FHWA/ USFWS/ GAEPD
Assessment of Effect Reports &
Air and Noise Studies
Preliminary Design
PFPR
Request permission to proceed to PFPR from OES
Tech Studies:
Agency Review/Approval
Technical
Studies
Cultural Resources
Ecology
Air & Noise
Notes: (click 1) The technical studies, including air & noise, must be approved by the appropriate agency. Same process as the resource ID reports.
(click 2) Once the technical studies are approved, or close to approval, the PM can request permission from OES to process to PFPR. The PM cannot submit the PFPR request without OES’s written permission.
(click 3) PFPR can then proceed.

## Slide 28: PDP Environmental Process (continued)
NEPA Document
Final design
ENV Permits (if needed)
FHWA Approval
NEPA Reevaluation (required)
PFPR corrections
Prelim. Design
FFPR
(ENV Approval Date)
Section 404; Buffer Variance; etc.
ROW Plan Approval
Notes: (click 1) After PFPR is held, the preliminary plans are updated to match the corrections from PFPR. While the design is being updated, the NEPA document is prepared.
(click 2) The NEPA document is submitted to FHWA for approval. After the PFPR plans are corrected, the ROW plans are finalized. However, the ROW plans cannot receive approval until the NEPA document is approved by FHWA.
(click 3) If permits are needed, they are being prepared and routed for agency concurrence simultaneously with preparation of the NEPA reevaluation.

## Slide 29: PDP Environmental Process
Let
Permit Approval
FHWA Approval
Environmental Certification
Note: Both must be approved for ENV certification
Final design
ENV Permits (if needed)
NEPA Reevaluation (required)
Section 404; Buffer Variance; etc.
FFPR
Notes: (click 1) Just like the NEPA document, the NEPA reevaluation must be approved by FHWA. The reevaluation documents any changes since the NEPA document was approved. If permits are needed, they are being routed for agency concurrence simultaneously with preparation and approval of the NEPA reevaluation.
(click 2) The project is ready to environmentally certify after the approval of the NEPA re-evaluation and the permits has been received. Note: the project cannot certify until both are approved.
(click 3) Then the project is environmentally ready to Let.

## Slide 30
EAOE or ERSRAOE
ERSR
Cultural Resource AOE
HRSR
Phase I Survey Report
SHPO
FHWA/ USFWS
Resource ID
Technical Studies
A3M
SHPO
*AOE = Assessment of Effect (impacts)
Ecology
Archeology
History
FHWA/ USFWS
Notes: As previously discussed, there are 2 steps to the special studies for ecology, archaeology and history. This graphic will explain the process of resource ID and technical studies. Air and Noise are not included because they do not have a resource ID report.
(click 1) The ecologist prepares the ecology resource survey report which goes to FHWA and US Fish & Wildlife Service for approval.
(click 2) The archaeologist prepares the Phase I survey report which goes to the state historic preservation office for approval.
(click 3) The historian prepares history resource survey report which goes to the state historic preservation office for approval.
(click 4) The A3M is held. Then the technical studies which document impacts can be written.
(click 4) The ecologist then documents the impacts to the resources in the Ecology assessment of effect report. Again this report is reviewed by FHWA and USFWS. For some projects, The ERSR is combined with the AOE. If it is combined, no document is submitted for agency review during the resource ID process.
(click 5) If there are any impacted resources for archaeology and/or history, one report is written. It is known as the cultural resource AOE. This report is approved by SHPO.

## Slide 31: Resource ID Process: ENV Field Survey
Environmental Field Survey is usually done during the concept phase.
Step 1 (aka ENV Field Work)
Visit the site
  Ecologist
  Historian
  Archaeologist
Physically evaluate for resources within the Environmental Survey Boundary (ESB)
Notes: (click 1) Environmental Field Survey/Resource ID is usually done during the concept phase.
Ecologist, Historian, and Archaeologist must visit the site.
These environmental SMEs must physically evaluate the project limits as defined in the Environmental Survey Boundary (ESB).
[next slide will explain the ESB]

## Slide 32
  Note: The ESB is 100 feet beyond the limits of construction and anticipated ROW. This is to allow minor design changes that may occur and avoid the need to go back to the field for additional surveys.
Resource ID Process: ESB
Notes:   (click 1) The environmental survey boundary is the area in which the environmental specialists conduct their studies. The ESB is drawn on a layout. It is usually drawn using a red line.
  Note: The ESB is 100 feet beyond the limits of construction and anticipated ROW. This is to allow minor design changes that may occur and avoid the need to go back to the field for additional surveys.

## Slide 33: Resource ID Process: Survey Reports
Step 2: Resource Survey Reports
Write resource reports
Receive agency approval of the resource reports
Notes: (click 1) Step 2 of the Resource ID process is the preparation of the resource survey reports which documents the findings of the environmental field work. The reports identify each resource that is located within the environmental survey boundary. After the reports are written by their respective environmental SME, the reports are submitted to the appropriate agency for review and approval.
[name of each special studies report is on next slide]

## Slide 34: Resource ID Process: Survey Reports
Ecology
Archaeology
History
ERSR
ASR or
Phase I Survey
HRSR
Notes:   (click 1)Ecology = Ecology Resource Survey Report (ERSR)
  (click 2) Archaeology =
    Archaeology Short Report (ASR) [if no resources are found] or
    Phase I Survey Report [if eligible or ineligible resources are found]
  (click 3) History = History Resource Survey Report (HRSR)

## Slide 35: Resource ID: Ecology
ERSR may be submitted to (FHWA/USFWS);
OR combined into the Ecology Resource Report and Assessment of Effects report (ERSRAOE).
  Note: If it is a combined report, ERSRAOE will not be submitted for agency approval until after A3M.
Notes: (click 1) ERSR may be submitted to Federal Highway Administration/US Fish & Wildlife Service (FHWA/USFWS). ERSR is the report that documents what ecology resources are located within the ESB;
(click 2) or it may be combined into the Ecology Resource Report and Assessment of Effects report (ERSRAOE). This document will report on the ecology resources found within the ESB and the proposed impacts to those ecology resources.
(click 3) Note: If it is a combined report, ERSRAOE will not be submitted for agency approval until after A3M.

## Slide 36: Resource ID: Cultural Resources
Phase I Survey Report and HRSR must be sent to the State Historic Preservation Office (SHPO) for concurrence.
  SHPO has the final decision regarding a resource being eligible or ineligible.
    Note: These are separate reports.
  Note: ASR is approved by GDOT.
Notes: (click 1) The Phase I Survey Report and HRSR must be sent to the State Historic Preservation Office (SHPO) for concurrence. These reports document the archaeology resources and the historic resources that are found within the ESB.
(click 2) SHPO has the final decision regarding a resource being eligible or ineligible.
(click 3) Note: These are separate reports. Remember that the HRSR is for historical resources and the Phase I Survey report is for the archaeological resources.
(click 4) Note: Archaeological Short Report ASR is approved by GDOT because there are no archaeological resources to document.

## Slide 37: Resource ID: A3M
A3M can be schedule when:
1. Agency concurrence(s) is received; and
2. Plans developed to show cut and fill limits (approx. 10% plans) are available
Note: Plans must show boundaries of all resources
Notes: (click 1) After the needed agency concurrence(s) is received for the resource survey reports, then the A3M can be scheduled when the plans have been developed to show cut and fill limits (approx. 10% plans). Note: The A3M plans must show the boundaries of all resources as identified during the Resource ID phase.

## Slide 38: Technical Studies
Begins after the A3M is held.
  Starts with P6 Activity 13417 (Receive Preliminary Plans to begin Technical Studies)
  Plans must incorporate all design changes from A3M.
Write reports about the impacts to the resources.
Notes:   (click 1) Environmental technical studies begin after the A3M is held. Starts with P6 Activity 13417 (Receive Preliminary Plans to begin Technical Studies). The designer will need to incorporate design changes into the plans as discussed at the A3M to avoid or minimize impacts before technical studies can begin.
  Environmental SMEs write reports about the impacts the project will have to any known resources as a result of the project’s design.

## Slide 39: Technical Studies
Technical Studies include 5 environmental disciplines:
  Ecology
  Archaeology
  History
  Air
  Noise
Notes: (click 1) Technical studies reports the impacts that are proposed for the environmental resources. There are 5 environmental disciplines that must write reports for the technical studies. The disciplines are ecology, archaeology, history, air, and noise.

## Slide 40: Technical Studies: Air & Noise
Air & Noise have separate reports.
Air & Noise reports are approved by GDOT.
  No agency concurrence is required.
Notes: (click 1) Air & Noise have separate reports. Air & Noise reports are approved by GDOT. Therefore, no agency concurrence is required.

## Slide 41: Technical Studies: Ecology
Assessment of Effect (AOE) are reports that discuss the project impacts
  how the impacts were avoided or minimized where possible
Ecology = Ecology AOE
  (or it could be a combined report: ERSRAOE)
  Report is approved by FHWA/USFWS
Notes: (click 1) Assessment of Effect (AOE) are reports that discuss the project impacts and how the impacts were avoided or minimized where possible.
(click 2) Ecology = Ecology AOE (or it could be a combined report: ERSRAOE). The report is approved by FHWA/USFWS

## Slide 42: Technical Studies: Cultural Resources
Archaeology and History are under a category called “Cultural Resources”
Archaeology and History impacts are combined into one report = Cultural Resource AOE
  Report is approved by SHPO.
Notes: (click 1) Archaeology and History are under a category called “Cultural Resources.”
(click 2) Impacts to archaeological and historical resources are combined into one report called the Cultural Resource Assessment of Effect (AOE). This is different than the resource ID reports which required separate reports for archaeology and history. The AOE report is approved by the State Historic Preservation Office (SHPO).

## Slide 43: Technical Studies & PFPR Request
OES permission to request PFPR is required.
OES will not concur to proceed to PFPR if they have not had a chance to review all of the technical studies reports.
Remember: To keep PFPR on schedule, start technical studies per Baseline Date.
Notes: (click 1) The PM must receive OES permission to request PFPR. Without the email concurrence, the PFPR request cannot be submitted.
(click 2) OES will not concur to proceed to PFPR if they have not had a chance to review all of the technical studies reports.
(click 3) To keep PFPR on schedule, start technical studies per Baseline Date.

## Slide 44
Which of the following conduct environmental field studies during resource ID? (hint: more than one answer)
Air
Archaeology
Ecology
History
Noise
Special Studies Review
Notes: (direction: Read question 1 and give participants time to respond)
(click 1) Answer: B, C, & D- Air & Noise do not got to the field or complete resource ID.

## Slide 45
Which of the following is NOT a True statement about resource ID?
The resources are incorporated into the plans.
History and archaeology have a combined report.
C. Ecology may prepare the ERSR or wait and prepare the
ERSRAOE.
D. The resource ID reports must be approved by the appropriate
agency.
Special Studies Review
Notes: (direction: Read question 1 and give participants time to respond.)
(click 1) Answer: B- History and Archaeology always have their own resource survey reports.

## Slide 46
The purpose of the resource survey report is to document the existing resources.
Special Studies Review
True
or
False
Notes: (direction: Read question 1 and give participants time to respond.)
(click 1) Answer: True

## Slide 47
Match the Word/Phrase & Definition
Special Studies Review
Resource Survey
Report
B. Technical Studies
Report
C. A3M
Documents the Impacts to resources
Discusses and implements design to avoid or minimize impacts to resources
Documents the resources within the ESB
Notes: (direction: Read question 1 and give participants time to respond.)
(click 1) Answer: A -3
(click 2) Answer: B-1
(click 3) Answer: C-2

## Slide 48
Which of the following have technical studies reports? (hint: more than one answer)
Air
Archaeology
Ecology
History
Noise
Special Studies Review
All of them
Notes: (direction: Read question 1 and give participants time to respond.)
(click 1) Answer: all

## Slide 49
PM does not need the permission of OES to request PFPR.
Special Studies Review
True
or
False
Notes: (direction: Read question 1 and give participants time to respond.)
(click 1) Answer: False - PM cannot receive permission from OES until the technical studies are complete. The PFPR request cannot be made without OES’s permission.

## Slide 50: Questions?