## Slide 1: Plan Reading Basics
09.18.2025
Office of Program Delivery
Notes: The training will provide a foundational level of understanding of how to read plans. It is intended for participants who do not have a roadway design background.
Training Time: 30 minutes

## Slide 2: Disclaimer
The goal of this course is to provide a broad overview for non-roadway designers to read, interpret and relate to a set of Transportation Roadway Design Plans. This course is not intended to override any official GDOT Plan Reading Courses. In the event of any discrepancy between the information presented within this course and any official GDOT Plan Reading Course, the GDOT Plan Reading Course shall prevail. For accurate plan interpretation, always use the current GDOT Policies and Procedures.

## Slide 3: Learning Objectives: How to Read
Plan Sheet Legend
ENV resources
Plan Sheet Numbering & Index Sheet
Coversheet information
CenterLine & Station Numbers
Notes: During this course, you will learn how to read
(click 1) the coversheet information
(click 2) plan sheet legend
(click 3) environmental resources and their boundaries
(click 4) roadway centerline and station numbers
(click 5) the plan sheet numbering and how it relates to the index sheet

## Slide 4
Plan Presentation Guidelines (PPG)
All roadway plans must follow the PPG
PPG is located on ROADS
  Manuals & Guidelines/Plan Presentation Guidelines/Category: PPG Current
Notes: (click 1) All projects that GDOT either designs or oversees the design work must follow the plan presentation guidelines. The PPG provides guidelines that are common to every section of the plans as well as specifics to a section of plans. The PPG can be accessed on ROADS and is available for the anyone to use including designers outside of GDOT staff.

## Slide 5
PPG Standards
All drawings must include the following standards:
  Use English Units
  Provide a scale for the plans
  Title Block
1” = 40 ‘
Notes: (click 1) All drawings (aka plans) must include the following standards: Using English units. For example, measurement is in feet and inches.
(click 2) The plan sheets must provide a scale to understand the true measurements of the design. The scale is to be consistent through out the plans. For example, a project may have 1 inch equals 40 feet. Therefore, if using a ruler on the plan sheet, if the segment of roadway is 8 inches long, this would be equivalent to 320 feet.
(click 3) A title block is required on each drawing. The block must include drawing number, PI number, U.S. & State route numbers with names of these roads.

## Slide 6
PPG Standards
All drawings must include the following standards:
  Centerline
Notes: (click 1) This is a line down the center of the proposed roadway that has increasing station numbers running from left to right. This will be discussed further on future slides.

## Slide 7
PPG Standards
All drawings must include the following standards:
  North Arrow
  Text Orientation
Notes: (click 1) A North arrow is placed on the upper part of the drawing. The reader must be able to orient the direction of the project.
(click 2) The text on the plan sheet should be read horizontal from left to right. When the text needs to be vertical, it should be placed parallel to the right edge of the drawing, reading from bottom to top of the drawing. These are not all of the PPG standards but are the ones that the PM should be reviewing when looking at a plan sheet.

## Slide 8
Coversheet
Required Information:
Project Owner
Project Description
Project Number (if applicable)
P.I. No.
State & Federal route number
County name
Notes: (click 1) Every set of plans has a coversheet. We will discuss some of the information that is required. Refer to the PPG for the complete list of requirements. The coversheet must include the name of the project owner. This is usually GDOT but could be another entity.
(click 2) The project description which matches the name listed on the PSR is included on the coversheet.
(click 3) The project number for older projects is included as well as the P.I. number and a list of any state or federal routes that the project involves.
(click 4) The county or counties where the project is located is also on the coversheet.

## Slide 9
Coversheet
Required Information:
Project Lenth Table
Revision Summary Table
Project map oriented with north at top of the drawing
Notes: (click 1) There is a table that provides length information related to net roadway length, net bridge length, net project length, etc.
(click 2) A table is included that is used to document revisions to the plans after they have been approved as a final set of plans.
(click 3) The project’s graphic must be oriented with north at the top of the drawing. To ensure that it is oriented correctly, a north arrow is included.

## Slide 10
Coversheet
Required Information:
Graphic representation Project Description
Congressional District(s)
Designation for “Plans prepared by”
Notes: (click 1) In the center of the coversheet, a graphic representation of the project is shown.
(click 2) The congressional district and the % of the project located in each district is included. This is because the GDOT Transportation Board members represent the different congressional districts.
(click 3) There is a section for the designer of the project. If it is designed by GDOT in-house, then it is the design engineer’s name. If it is designed by a consultant, it is the consulting firm and designer. The engineer must mark the plans with their professional engineering stamp.

## Slide 11
Coversheet
Required Information:
Designation for “Recommended for acceptance by:”
Chief Engineer signature & date
Project Location Map
Notes: (click 1) The designation of recommended for acceptance by must always be on the coversheet. For OPD projects, the title under the signature line will State Program Delivery Administrator.
(click 2) A box will be included for GDOT’s Chief Engineer to sign and date when the plans are finalized.
(click 3) In the top left corner will be a high-level project location map with a north arrow to orienting the location.

## Slide 12
Coversheet
Standard Information:
Scale
Drawing No
Notes: (click 1) As previously stated, there are some standard requirements that apply to the coversheet. A scale that can be used with the project graphic is included.
(click 2)The drawing number is included in the lower right corner. The coversheet is a plan sheet. It is always the first sheet.

## Slide 13
Legend
Notes: (click 1) On the design set of plans, there will always be a legend located in the lower left corner of the plan sheet.

## Slide 14
Legend
Notes: (click 1) This is an example legend from PI 0009949. This is typical of a legend used on the main line set of plans. The main line set are the plans that show the construction of the roadway work. As you can see, the plans include existing property lines and required right-of-way lines. [click to transition to next slide to show an example]

## Slide 15
Legend
Notes: (click 1) (to highlight property line and required ROW line)

## Slide 16
Legend
Notes: (click 1) The mainline plans must include the construction limits. A dashed line with a “C” or a “F” represents where the existing land must be cut (or soil removed) which is represented with a “C”. The “F” line represents filling in the land (or adding soil) to raise the elevation.

## Slide 17
Legend
Notes: (click 1) The “C” line on this plan sheet is showing the limits of cutting the earth. The yellow is representing that the land up to this line will be cut (aka lowered in elevation).
(click 2) The dark purple is highlighting the “F” or fill line. The pink is representing that the land up to this line will be filled in with additional soil (aka raising the elevation).

## Slide 18
Legend
Notes: (click 1) Various types of easements may be used on a project during construction. Easements are portions of land that GDOT does not own. The easement provides access to someone’s property or portion of a property during construction. Some easements are temporary which means that after the project is constructed, GDOT does not have the right to do any work on the property owner’s land. Other easements are permanent which means that after construction the land returns to the property owner but GDOT has paid for the right to be able to access that parcel or portion of the parcel in the future if work to maintain or repair the roadway is needed in the future. Permanent easement avoids the need to meet with the property owner and negotiate access to the land in the future.

## Slide 19
Legend
Notes: (click 1) These are examples of easements for constructing a driveway. Driveways need to have access to the roadway in which they join to. If the roadway lowers or raises the elevation, the driveway would no longer be able to have proper access to it. To solve the problem, the designer will include a temporary easement for the contractor to be able to work on the driveway to ensure its access to the roadway. After the project, GDOT would no longer be responsible for maintaining the driveway because the ownership will have fully returned to the property owner.
(click 2) According to the legend, this is an easement for the construction of slopes. It could be temporary or permanent easement. The ROW specialist will determine this during negotiations with the property owner.

## Slide 20
Legend
Notes: (click 1) Environmental specialists (ecologist, archaeologist, & historians) have completed the field work and resource ID which determined if any resources were present and the boundaries of each resource. This information was then shared with the designer who placed the resources on the plan sheet. Then the designer engineered the plans to avoid or minimize the impacts to the resources. The boundary of any resource is shown on the plans as an ESA (Environmental Sensitive Area).

## Slide 21
Legend
Notes: (click 1) This is always represented with a line with triangles. The triangles always point in towards the resource. In this example, it is pointing to the stream. This is the buffer that provides a protective zone around the stream.
(click 2) Anything inside of this area is the resource as visually represented by the green lines. Anything outside of the line is not a resource.

## Slide 22
Legend
Notes: (click 1) Orange barrier fence is installed on a project to let the contractor know that they cannot work beyond this area. It is installed as measure to avoid or reduce impacts to an environmental resource on a project. Without the OBF, the contract has the right to work up to the required ROW limits. The orange barrier fence is always represented with a line that has solid black circles.

## Slide 23
Legend
Notes: (click 1) The blue highlight is following the required ROW line.
(click 2) The pink highlight is following the ESA boundary. Remember that the triangles on the boundary line point inwards towards the environmental resource.
(click 3) The orange highlight is over the orange barrier fence which is represented with a line and solid circles.
(click 4) The orange shaded area is protected from the construction work because it does not allow the contract to work up to the required ROW line. T
(click 5) The blue shaded area is being impacted by construction. The contract is allowed to work up to the OBF. This portion of the resource is within the construction limits. Because some of the resource was protected, it shows that impacts were minimized where they could be.

## Slide 24
CenterLine & Station Numbers
Centerline
Marks the middle of the roadway
Serves a reference point
Notes: (click 1) All design sheets must display the centerline of each roadway segment that is being involved with the construction of the project. The centerline is a line that marks the middle of the proposed roadway. It serves as a reference point for aligning the road’s geometry and for establishing consistency in the design and construction of the road.

## Slide 25
CenterLine & Station Numbers
Station Numbers:
Provide a measurement of distance
Increase in numbering from left to right or bottom to top
100 feet
Notes: (click 1) Station numbers are located on the centerline and are marked with a 90-degree line. Longer marks indicate 100 feet between two consecutive long marks. At every 100 feet, a Station Number will be labeled on the plans.
(click 2) The station numbers increase from left to right or bottom to top of the drawing.

## Slide 26
CenterLine & Station Numbers
Station Numbers:
Provides the location of features and design elements
Indicate if station is right or left (side of drawing)
  RT
  LT
i.e. Driveway
STA. 240+35
LT
RIGHT
LEFT
Notes: (click 1) The station numbering is also used to reference the location of a feature or design element. In this example, this driveway is located at approximately station 240+35. Remember that the numbers increase from left to right or bottom to top. The next station is 100 feet away. This driveway is a little less than halfway to the next station. The short line indicates the 50-foot mark. Since I did not see a label with the station number on the driveway, I estimated it to be about 35 feet after station 240.
(click 2) There are 2 sides to the centerline: a right side and left side. Right or left side is determined by looking at the plans and seeing the increasing station numbers. Just giving a station number, does not tell me which side of the centerline the feature or design element is located. Therefore, as part of the reference of the location RT or LT must be included. For this example, the driveway would be STA. 240 + 35 RT.

## Slide 27
Plan Section sequence
Section Sequence:
Specific order for the plans
Represented by 2-digit number
Plan sections range from 01- 60
  Not every project requires all sections
Excerpt of PPG Section 1.2.1
Notes: (click 1) Construction plans are comprised of sections of drawings. Per the PPG, there is a specific order to the sequence and a two-digit number associated with each section. The graphic on this slide is an excerpt from the PPG manual section 1.2.1.
(click 2) Per the PPG, there are up to 60 sections of the plans. The numbering begins with “01”. Not every project will require all 60 sections. The need for various drawings will vary from project to project.

## Slide 28
Plan sheet Numbering
Drawing Number
Format XX – XXXX
  Series
  Sheet Number
Notes: (click 1) Per the PPG, each plan sheet must be numbered using the format of 2 digits for the series number and 4 digits for the sheet number. There may be multiple sheets within a set of the series (aka section). Collectively, this is referred to as the drawing number. It is always found in the lower right corner of each plan sheet. The drawing numbers will be shown on every drawing and will never change after the final plans have been submitted to the Office of Bidding Administration.

## Slide 29
Index Drawing
Index Drawing:
Identifies the plan contents
Format 02 – XXXX
Notes: (click 1) The index drawing is required for each set of construction drawings to identify the plan contents. Think of it as a table of content for the set of plans. The index should list all plan sections. Drawings are grouped according to the sequence of the plans. In other words, the drawings are listed in numerical order by section.
[next slides will enlarge the image to make it easier to read]

## Slide 30
Index Drawing
Notes: (click 1) This is an example index drawing from PI 0009949. The series and the sheet numbers for the pages of each section are listed in numerical order.
[next slide will zoom in and teach how to read the index]

## Slide 31
Index Drawing
Cross reference dgn & pdf files before submitting the plan set
Notes: (click 1) The index is telling the contractor that there 2 plan sheets in the Index section of the plans.
(click 2) The index is telling the contractor that there are no 12 series drawings. Also, it is letting them know that there are 6 drawings for the mainline plans.
(click 3) As a PM, when receiving the plans, the dgn and pdf files should be cross reference with the index drawing to ensure that all files have been provided.

## Slide 32
Index Drawing
Notes: (click 1) As previously discussed, the drawing number is located in the lower right corner of every plan sheet. Even the index sheet has a drawing number. By referencing, the index information, the contractor will know that this is the first of two plan sheets for this section.

## Slide 33: Questions?